## Slide 1
Notes: A fully-actuated unmanned aerial vehicle serves as the experimental platform to execute physical interaction tasks.
[Sliding Bbox · SciMMIR_arch_diff_000000348 · frame_0003.png · 1.476s]

## Slide 2
Notes: The onboard force-torque sensor at the manipulator base provides direct force measurements at sixty hertz.
[Sliding Bbox · SciMMIR_arch_diff_000000348 · frame_0007.png · 5.167s]

## Slide 3
Notes: At the end-effector tip, a GelSight vision-based tactile sensor captures optical tactile images at thirty hertz.
[Sliding Bbox · SciMMIR_arch_diff_000000348 · frame_0011.png · 8.858s]

## Slide 4
Notes: Optical flow tracks the motion of printed markers to capture the deformation of the elastomer gel pad.
[Sliding Bbox · SciMMIR_arch_diff_000000348 · frame_0015.png · 12.554s]

## Slide 5
Notes: A k-nearest neighbors model then estimates the contact force directly from these marker displacement features.
[Sliding Bbox · SciMMIR_arch_diff_000000348 · frame_0019.png · 16.246s]

## Slide 6
Notes: A Kalman filter fuses the force-torque sensor measurements and tactile estimates to obtain the measured contact force.
[Sliding Bbox · SciMMIR_arch_diff_000000348 · frame_0023.png · 19.937s]

## Slide 7
Notes: In parallel, a ResNet-18 neural network processes the full tactile image to determine contact and recognize surface textures.
[Sliding Bbox · SciMMIR_arch_diff_000000348 · frame_0027.png · 23.628s]

## Slide 8
Notes: The classification output identifies the contact texture and generates a discrete contact detection switching signal.
[Sliding Bbox · SciMMIR_arch_diff_000000348 · frame_0031.png · 27.324s]

## Slide 9
Notes: A motion capture system provides high-rate position measurements at one hundred eighty hertz.
[Sliding Bbox · SciMMIR_arch_diff_000000348 · frame_0035.png · 31.015s]

## Slide 10
Notes: The force controller computes the force tracking control effort using the fused contact force and reference force.
[Sliding Bbox · SciMMIR_arch_diff_000000348 · frame_0039.png · 34.706s]

## Slide 11
Notes: Simultaneously, a position controller calculates the motion control command based on reference and measured positions.
[Sliding Bbox · SciMMIR_arch_diff_000000348 · frame_0043.png · 38.398s]

## Slide 12
Notes: A selection matrix dynamically blends the motion and force control commands based on the contact detection state.
[Sliding Bbox · SciMMIR_arch_diff_000000348 · frame_0047.png · 42.091s]

## Slide 13
Notes: Finally, the control allocation module maps the combined wrench command into individual rotor speeds for the fully-actuated vehicle.
[Sliding Bbox · SciMMIR_arch_diff_000000348 · frame_0051.png · 45.785s]